## Slide 1
AgriNova
An FPGA + Arduino smart-farm guardian with a Telegram remote control
Motion security · Soil monitoring · Automated watering · Live camera evidence

## Slide 2
Synopsis
AgriNova is a low-cost, distributed farm-monitoring system. A VSDSquadron FPGA Mini runs pure-hardware Verilog logic that watches an IR beam; an Arduino UNO reads soil moisture, temperature and humidity, and drives a servo and the mist-maker relay; a Mac acts as the cloud gateway, bridging both boards to the Telegram Bot API; and a Windows VM contributes webcam photo and video capture. The farmer arms or disarms the farm, requests photos and clips, and receives soil and intruder alerts — all from a Telegram chat.
4
hardware nodes
FPGA · Arduino · Mac · Windows VM
8
Telegram commands
from /lockdown to /video
10 s
IR alert cooldown
burned into FPGA silicon
0
cloud servers
the Mac IS the cloud gateway
Built after the original ESP32 died — its failure became the project's best design decision.

## Slide 3
Why AgriNova?
Farms are unattended most of the day
Intruders — human or animal — walk in unnoticed. There is no one watching the gate at 3 a.m.
Watering is guesswork
Crops are over- or under-watered because nobody measures the soil; moisture changes hour to hour.
Alerts arrive too late
By the time damage is discovered, the event is hours old. Farmers need the alert the moment it happens.
Commercial systems cost too much
Off-the-shelf farm IoT is subscription-priced. AgriNova uses hobby boards and a chat app the farmer already has.

## Slide 4
System architecture
IR sensor
beam-break detection
(active LOW, pin 38)
Status LEDs
blue = IR live, green = TX
Soil + DHT11
A0 moisture · A1 temp/RH
Servo A3 · Mist relay A2
both on external 5V
VSDSquadron
FPGA Mini
Verilog: UART TX, IR edge
detect, 10 s cooldown
@ 12 MHz
Arduino UNO
soil + DHT11 every 5 s
MIST_ON / MIST_OFF /
ROTATE / STOP commands
Mac bridge
(Python)
serial listeners · Telegram
polling · camera job relay
· alert throttling
Telegram
commands in,
alerts + media out
Windows VM
webcam photo &
video capture
UART 9600
UART 9600
Bot API
polls jobs
Every camera connection is Windows → Mac: the VM long-polls for jobs, so no inbound firewall holes are needed.

## Slide 5
How it works — hardware logic on the FPGA
There is no CPU and no firmware on the FPGA — every behaviour is synthesized digital logic clocked at 12 MHz:
Baud generator
A counter emits one tick every 1,250 clock cycles — exactly 9600 baud for the UART transmitter.
IR edge detector
The sensor line is double-synchronized; a falling edge (beam broken) fires one alert request.
Hardware cooldown
A 120-million-cycle countdown (10 s) blocks repeat alerts while the beam stays blocked.
Message sequencer
A request/acknowledge handshake feeds the bytes I R \n into the UART, one per frame.
Single purpose
No CPU, no firmware, no OS to crash — the intruder detector is pure logic that cannot hang.
Status LEDs
Blue mirrors the IR sensor live (instant wiring check); green flashes on every UART transmit.
Toolchain: Verilog → yosys → nextpnr-ice40 → icepack → iceprog (fully open source)

## Slide 6
How it works — the Mac bridge & camera relay
1
Listen
Two serial threads read the FPGA and Arduino; both auto-reconnect if a USB cable is pulled.
2
Filter
Soil updates are throttled to one per 10 minutes — but a wet/dry flip alerts immediately.
3
Decide
Intruder alerts only fire while the farm is armed with /lockdown; /unlock silences them.
4
Capture
On alert or /photo, a job is queued; the Windows VM polls it, shoots, and posts bytes back.
5
Deliver
Photos and clips are uploaded to Telegram as proper multipart form-data with captions.
Key trick: the camera link is reversed. Windows polls the Mac for work, so macOS privacy walls and Windows firewalls never block it.

## Slide 7
The farm in your pocket — Telegram commands
/lockdown
Arm the farm — IR intrusion alerts + automatic 5 s evidence clip
/unlock
Disarm — walk the farm without spamming your own phone
/photo
Instant webcam snapshot, captioned with date and time
/video 5…30
Record a clip of chosen length and deliver it to the chat
/mist_on /mist_off /spray N
Fire the mist maker via the Arduino relay — manual or timed burst
auto: soil + climate
Moisture, temperature & humidity every 10 min — instantly on a wet/dry flip
auto: intruder + tamper
Alert + clip + 10 s mist burst; camera yanked mid-clip → CRITICAL alert
/rotate, /about, /stop…
Servo control, help text, global alert mute / resume
Every interaction happens in a plain Telegram chat — no app to install, no dashboard to host.

## Slide 8
Battle scars — problems we engineered around
ESP32 regulator death
Problem: The original Wi-Fi board boot-looped from a failed regulator
Fix: Pivoted to FPGA + host-bridge design — more robust than the original plan
macOS blocked the VM
Problem: Local-Network privacy silently dropped every Mac → VM packet
Fix: Reversed the flow: Windows long-polls the Mac — nothing inbound to block
Corrupt photo uploads
Problem: Hand-rolled multipart body had a stray boundary — HTTP 400
Fix: Rebuilt the encoder; photos and videos now upload reliably
Servo refused to move
Problem: Arduino's 5 V rail cannot source a servo's ~500 mA stall current
Fix: Signal from A3, power from a dedicated external 5 V supply
Fast-forward videos
Problem: Clips played at 30 fps though the VM webcam delivered far fewer
Fix: Measure the real frame rate, write the file at that rate — true 5 s clips
Phantom motion spam
Problem: A floating echo pin invented intruders every few seconds
Fix: Removed the disconnected sensor; alerts are gated behind /lockdown

## Slide 9
It works — the intruder scenario, end to end
0.0 s
Something crosses the IR beam at the farm gate
+0.000 01 s
FPGA edge detector fires; blue LED lights; cooldown starts
+0.01 s
“IR\n” leaves the UART at 9600 baud toward the Mac
+0.5 s
Bridge (armed via /lockdown) posts “🚨 Someone is in your farm!”
+1 s
Mist relay fires for 10 s; a video job is queued for the Windows VM
+8 s
A real-time 5 s clip lands in Telegram as “🎥 Intruder clip”
Also verified live: /photo, real-time /video, throttled soil telemetry, USB hot-unplug recovery, camera-removal CRITICAL alert.

## Slide 10
What's next
Soil calibration
Field-calibrate the probe so the 40% wet/dry threshold tracks real soil.
Smart irrigation
A second relay on a pump, driven by the soil reading, closes the loop.
Live video feed
/live streams the farm in real time — flipbook frames in chat, or MJPEG over Tailscale.
CV crop doctor
A vision model on the camera feed flags pests and abnormal growth.
Tamper hardening
Camera-removal alerts exist; add heartbeat alerts for each board going offline.
The architecture already supports all five — each lands as a new sensor wire or a new bridge handler.

## Slide 11
A farm that texts you back.
AgriNova — hardware-level reliability, chat-level simplicity.
github.com/rohancodesss/agrinova
rohancodesss.github.io/agrinova